Bioinformatics III
Analysis and prediction of 3D macromolecule structures
Experimental methods for 3D structure determination
Saulius Gražulis
2024 m.

---
Methods to obtain structural information
- X-ray neutron crystallography
- NMR
- CryoEM (Cryo Electron microscopy, multiple particle analysis, electron tomography)
- Electron diffraction
- EM (Electron microscopy, negative staining)
- SAXS/SANS – Small Angle X-ray/Neutron Scattering
- EXAFS, XANES
- ...

---
CryoEM
Image taken from: (Murata & Wolf, 2018) CC BY

---
SPA & CryoET
SPA (Single Particle Analysis)
ET (Electron Tomography)
Paveiksliukas iš: (Murata & Wolf, 2018) CC BY

---
CryoEM electron density
Image taken from: (Murata & Wolf, 2018) CC BY

---
Diffraction experiment
Cu, Mo, Au, ...

C

Pb
e-
Be
 ≃ 1Å

---
X-ray sources
Syncrotrons (particle accelerators)
X-ray tubes
N

Cu, Mo, Au, ...
S
e+

e-
Be

---
Goniometer head

---
A diffraction image

Pb

---
Properties of reflections
Each reflections has:
an amplitude (of the electric field);
and phase (delay with respect to other reflections);
Both of these parameters depend on a structure factor.

---
Properties of reflections
The reflection positions (i.e. reflection angles) depend only on the lattice parameters;
The intensities of the reflections depend on the conetnts of the unit cell.

---
A complete dataset
When a crystal is rotated, some reflections appear, and some others vanish.
After max. 360° rotation reflections start repeating themselves (maybe sooner, especially if the crystal is highly symmetric).

---
Properties of a dataset
- Resolution
- Completeness
- Multiplicity
- Signal-to-noise ratio (Rmerge, I/I)

---
A model might not be unique!
Example:
m
A mirror image of a structure has (nearly) identical diffraction pattern (identical if there is no anomalous scattering)

---
Electron density to model

---
Rankinis modelio konstravimas

---
Automatiniai modelio konstravimo įrankiai

---
Prior information is essential!
- Number of molecules in the asymmetric unit
- Protein size and sequence
- Structures of amino acids ;-)
- Composition of crystallisation conditions (ions, buffers)
- Protein production and purification method

---
Structure refinement
- Lest squares method
- Maximum likelihood methods
- Bayesian methods

---
Refinement criteria
Crystallographic R-factor:
R_{cryst} = SUM_{h k l} \lline F^{obs}_{hkl} - F^{calc}_{hkl} \rline / SUM_{h k l} \lline F^{obs}_{hkl} \rline
R-free:
~10% (test set)
R_{free} = SUM_{h k l %element Test set} ...
hkl
~90% (working set)
R_{cryst} = SUM_{h k l %element Working set} ...

---
Parameters
- Aromic coordinates
- Thermal displacement parameter(s) (B-factors)
- Occupancies
Important to know: the observation-to-parameter ratio

---
Structure quality indicators
- Resolution (Å)
- R factor (full, crystallographic), Rcryst
- „Free“ R factor, Rfree
- Rfree - Rcryst, Rcryst/Rfree
- Rcryst and Rfree in the outer resolution shell
- Average error of bond lengths and angles

---
Non-polymeric molecules
- Solvent (water!)
- Ions
- Ligands, cofactors
- Modified amino acids and/or DNA/RNA bases

---
Evidence of chaos
- Zero occupancies
- Huge B-factors
- Residues without the side chains

---
Resources in the Net
Protein Data Bank (PDB)
http://www.rcsb.org/pdb/
Macromolecular Structure Database http://www.ebi.ac.uk/msd/
International Union of Crystallography http://www.iucr.org/
Crystallography Open Database (COD) http://www.crystallography.net/